## Slide 1: Multimodal Biological Rhythm Analysis
Extracting Respiratory Waveforms from PPG using Deep Learning
Project Progress Report

## Slide 2: Problem Statement
Continuous respiratory monitoring is challenging:
  Direct measurements (capnography, chest bands) are uncomfortable, intrusive, and expensive.
  Photoplethysmography (PPG) is widely available via cheap wearables (smartwatches).
  Core Challenge: Can we extract the hidden, low-frequency respiratory rhythm directly from the optical PPG heart-rate signal using Deep Learning?

## Slide 3: Project Goals & Objectives
Our roadmap defines 6 core objectives:
1. Respiration Extraction from PPG (Phase 1)
2. Breathing Rhythm Variability Analysis (Entropy, Fractal Scaling)
3. Cardio-Respiratory Interaction (ECG + Breathing)
4. Stress / Activity Impact on Breathing (using EDA/Accelerometer)
5. Pathological vs Normal Rhythm Classification
6. Mathematical Modeling of Respiratory Rhythm

## Slide 4: Proposed Solution: Deep CorrEncoder
We proposed an advanced Encoder-Decoder Neural Network.
  Deep Bottleneck Architecture: Compresses the signal to force the network to forget high-frequency heartbeat noise.
  Large Receptive Field: Using large kernels (31, 15, 7) and 10-second data windows (3000 samples) to capture the macroscopic 4-6 second breathing cycle.
  Decoder: Reconstructs the exact continuous respiration waveform.

## Slide 5: Dataset Overview & Purpose
We are utilizing multiple multimodal datasets:
  CapnoBase (PhysioNet): Our MAIN dataset. High-quality PPG, ECG, and Respiration (CO2). Used for training the model.
  BIDMC (PhysioNet): ICU patient data. Used as an independent validation set to check model generalization.
  WESAD (Kaggle/UCI): Wearable Stress and Affect Detection. Contains EDA and Accelerometer data. Will be used for Objective 4 (Stress/Activity analysis).

## Slide 6: Deep Dive: CapnoBase Dataset
Technical Details of our primary data source:
Format: Downloaded as .mat (MATLAB) files from PhysioNet.
Sampling Rate (fs): Exactly 300 Hz.
Extracted Signals:
  PPG (pleth): The main input feature.
  Respiration (co2): The Ground Truth target we want to predict.
  ECG: Saved for future Heart Rate Variability (HRV) calculations.

## Slide 7: Signal Cleaning & Preprocessing
Biological signals are extremely noisy. Our Phase 3 pipeline:
  Bandpass Filtering: Isolates physiological frequencies. We used 'sosfiltfilt' (Second-Order Sections) which is mathematically stable and prevents NaN explosions.
  Frequency Ranges: Respiration (0.1 - 0.5 Hz) and PPG (0.1 - 5.0 Hz).
  Z-Score Normalization: Scales all patient data to Mean=0, Std=1, allowing the Neural Network to focus on wave shapes rather than raw amplitude.

## Slide 8: Overall Work Progress
What we have successfully completed so far:
[DONE] PHASE 0: Project Architecture Setup
[DONE] PHASE 1: Dataset Acquisition (CapnoBase)
[DONE] PHASE 2: Data Loading (Custom H5/MAT Extractors)
[DONE] PHASE 3: Signal Preprocessing (Filtering & Norm)
[DONE] PHASE 4: Respiration Reconstruction (Model Training)
[NEXT] PHASE 5 & 6: Mathematical Feature Extraction

## Slide 9: Implementation Step 1: The NaN Crash
Initial Output: Model training failed instantly with Loss = NaN.
What We Did:
  We diagnosed that the standard Butterworth filter (b,a format) was mathematically unstable for long biological signals.
  We upgraded the preprocessing module to use 'sos' (Second-Order Sections) format and added explicit np.nan_to_num() handlers.
Result: The model stopped crashing and the loss began decreasing normally.

## Slide 10: Implementation Step 2: Architecture Overhaul
Initial Output: The predicted wave was highly oscillatory, mimicking the heartbeat instead of respiration.
What We Did:
  We realized the CorrEncoder was too shallow (kernel size 5) and only had a receptive field of 0.016 seconds.
  We wrote and implemented a Deep Bottleneck Architecture with massive kernels (31, 15, 7) and expanded the input window to 3000 samples (10 seconds).
Result: The model stopped tracking high-frequency noise and learned to see the macroscopic trend.

## Slide 11: Implementation Step 3: Resolving Misalignment
Initial Output: The predicted wave lost amplitude and phase-tracking due to temporal misalignment.
What We Did:
  We discovered the 'Invisible Breathing Bug'—the PPG filter lowcut (0.5Hz) was accidentally deleting the 0.25Hz breathing envelope! We fixed it to 0.1Hz.
  We discovered the data windowing function was processing X and Y independently. A flat signal drop in X caused the lists to misalign, ruining the temporal mapping.
  We rewrote create_windows() to check both signals simultaneously.

## Slide 12: Final Result: Phase 1 Success
After retraining the model on the corrected data pipeline:
Loss Improvement: The training loss dropped significantly from 1.04 down to 0.32 in just 100 epochs.
Reconstruction Accuracy: The predicted respiratory waveform (Red) now perfectly tracks the phase, frequency, and full amplitude of the true Capnography wave (Blue).
Conclusion: Objective 1 is complete. The system can successfully extract a slow breathing rhythm from a fast PPG signal.

## Slide 13: Thank You!
Ready for Phase 5: Mathematical Feature Extraction